## Slide 1: Mechanistic-Empirical Pavement Design Implementation in Michigan
APAM Annual Paving Conference
April 21-22, 2015
Mt. Pleasant, MI
Michael Eacker, MDOT
Justin Schenkel, MDOT

## Slide 2: Outline
What is ME?
ME Timeline/Work to Date
Calibration
MDOT Implementation/Transition
Preliminary Phase Design Results
Transition Phase 1
ME Webpage

## Slide 3: What is ME?

## Slide 4: What is ME?
Mechanistic-Empirical pavement design (ME) is the latest generation of pavement design methodology
Mechanistic: uses the theory of mechanics - pavement response (stresses/strains) to applied load
Empirical: observations (actual performance) used to calibrate the mechanistic models

## Slide 5: What is ME?
Structure
& Materials
Traffic
Mechanistic
Analysis
Transfer
Functions
Predicted
Performance
Climate
EICM*
* - Enhanced Integrated Climatic Model

## Slide 6: What is ME?
 | AASHTO 1993 | Mechanistic-Empirical
Basis | Empirical observation from the 1958-59 AASHO Road Test | Theories of mechanics
Original Calibration | AASHO Road Test – Ottawa, Illinois | SHRP test sections from around the country
Traffic Characterization | Equivalent Single Axle Load | Axle load spectra
Materials Inputs | Very few | Many
Climatic Effects | Limited – can change inputs based on season | Integral – weather data from 600+ US weather stations included
Performance Parameter | Present Serviceability Index | Various distresses, IRI
Output | Thickness | Performance prediction (distress prediction)

## Slide 7: What is ME?
Axle Load Spectra

## Slide 8: What is ME?
Examples of new materials inputs
    Gradations, liquid limit, plasticity index, optimum water content, etc. of base/subbase/subgrade
    Thermal properties of the paved surface (expansion, conductivity, heat capacity)
    Concrete shrinkage (ultimate, reversible, and time to 50%), unit weight, cement content, water to cement ratio, etc.
    HMA air voids, binder content, unit weight, dynamic modulus, creep compliance, IDT, etc.

## Slide 9: What is ME?
Weather Stations

## Slide 10: What is ME?
Distresses (performance) predicted over time
  HMA distresses
    Transverse cracking
    Longitudinal cracking (top-down)
    Fatigue cracking (bottom-up)
    Rutting
    IRI
  Concrete distresses
    % slabs cracked
    Faulting
    IRI

## Slide 11: What is ME?
Iterative design process:
  Enter initial cross-section
  Run the design
  Review the results
  Adjust as necessary until an acceptable design is found

## Slide 12: ME Timeline/ Work to Date

## Slide 13: ME Timeline
1986
1998
2004
2005
2006
AASHTO Pavement Design Guide includes recommendation to move toward mechanistic design
NCHRP project 1-37A (“AASHTO 2002”) begins
NCHRP project 1-37A completed
Version 0.8 of the software
Evaluation of 1-37A Project
Concrete CTE Project
MDOT Research 

## Slide 14: ME Timeline
2007
2008
2009
2010
2011
2012
2014
2013
Version 1.0 of the software released
Accepted as AASHTO’s interim design method
DARWin-ME becomes available from AASHTO
Software re-branded as Pavement ME Design
Development of commercial version of software (2.0) begins
Evaluation of 1-37A Project
Concrete CTE Project
Traffic Characterization Project
Unbound Materials Resilient Modulus Project
Subgrade Resilient Modulus Project
HMA Characterization
Rehab Design Sensitivity
ME Calibration
Packaged as one project

## Slide 15: Work To Date
Other on going work
Improvement of Michigan Climatic Files in Pavement ME Design
  Current research project with completion date of April 30, 2015
  Clean up the data
    Fill in missing months
    Correct errors
  Add additional years of data
  Sensitivity to weather stations, weather data, and number of years of data
  Recommend locations for new stations

## Slide 16: Work To Date
Traffic and Data Preparation for AASHTO MEPDG Analysis and Design
  National pooled fund study
  Developed software for converting PTR data to ME inputs (replaces TrafLoad)
  Also runs quality checks on the data and tools for repairing/improving the data

## Slide 17: Work To Date
ME Oversight Committee
  Goal: Facilitate the implementation of ME as MDOT’s standard design method
  Facilitate business process changes for pavement design
  Help with decisions on design criteria
  Help with decisions on input values
  Expand department knowledge of the software and the impacts of different inputs and design decisions
  Explore research needs
  Facilitate industry participation

## Slide 18: Work To Date
ME Oversight Committee (cont.)
  Membership from various areas
    Supervisors of the following general areas:
      Pavement management
      HMA materials
      Concrete materials
      Aggregate materials
      Pavement evaluation
      Traffic monitoring
    Pavement Operations Engineer
    Pavement Design Engineer (chair)
    Region Soils Engineers (Region pavement designers)
    Concrete and HMA paving industries

## Slide 19: Calibration

## Slide 20: Calibration
Concept: Use Michigan Pavement Management System (PMS) data and project specific inputs to calibrate the ME distress prediction models
Goal: Minimize the error between observed and predicted distresses, and eliminate bias

## Slide 21: Calibration
Measured
Predicted
We want the data to plot as close as possible to this line

## Slide 22: Calibration
Example of minimizing error

## Slide 23: Calibration
Example of bias

## Slide 24: Calibration
Source: Final report RC1595
Default Calibration
Michigan Calibration

## Slide 25: Calibration
Conducted by Michigan State University
Projects involved in calibration:
  HMA reconstruct – 85
  Concrete reconstruct – 20
  Rubblize – 11
  Unbonded concrete overlay – 8
  Crush and shape – 23
  HMA overlay – 22
LTPP projects from Michigan, Ohio, and Indiana were added in to see if the calibration could be improved

## Slide 26: Calibration
Reviewed construction projects records from long-term storage for materials inputs
Used as many as-constructed inputs as possible to create ME designs for all projects used for calibration
Predicted distresses pulled from the ME results and compared to the observed data
Were able to improve all distress models

## Slide 27: Implementation/Transition

## Slide 28: Implementation/Transition
Transition Phases:
  Preliminary phase – ME designs of recent life-cycle projects
  Phase 1 – newly submitted life-cycle and APB reconstruct projects
  Phase 2 – Region-designed reconstruct projects
  Phase 3 – newly submitted life-cycle rehab projects
  Phase 4 – Region-designed rehab projects
  Phase 5 – final recommendations for full implementation

## Slide 29: Implementation/Transition

## Slide 30: Preliminary Phase Design Results

## Slide 31: Preliminary Phase Design Results
The Preliminary Transition Phase involves using the calibration results on recently life-cycled reconstruct projects to see the design produced by ME
13 life-cycled reconstruct projects from 2012 - 2014 were included
  Projects from all Regions except Superior were included
  Designs include ramps if they were included in the original life-cycle
  Using inputs agreed upon by the ME Oversight Committee and Subcommittees and the final calibration coefficients
  Life-cycles were re-run with the final ME cross-section

## Slide 32: Preliminary Phase Design Results
Two sets of design results:
  Disregarding typical minimum pavement thicknesses
  With minimum thickness standards and ±1” restriction
    ±1” restriction (NEW): AASHTO 1993 design used for the initial cross-section in ME. Final ME design cannot vary from this by more than 1”.

## Slide 33: Preliminary Phase Design Results

## Slide 34: Preliminary Phase Design Results

## Slide 35: Preliminary Phase Design Results

## Slide 36: Preliminary Phase Design Results
Average thickness change from original designs used in life-cycle:
  Concrete: -0.05”
  HMA: -0.28”
  Average includes the designs that did not change due to minimum pavement thicknesses
These final designs were plugged into the original life-cycles

## Slide 37: Preliminary Phase Design Results
Life-cycle results:
  Results from all 13 projects were the same – original low cost alternative did not change
  Difference between the two options was closer on 5 projects
  Difference between the two options was wider on 4 projects
  Four projects did not have thickness changes (minimum thickness standards) – life-cycle not re-run

## Slide 38: Preliminary Phase Design Results
Life-cycle results (cont.):
  Changes in life-cycle initial construction costs
 | 9 Re-run LCCA’s | All 13 LCCA’s | Interstate | Non-Interstate
HMA | -0.7% | -0.5% | -13.9% | +0.9%
Concrete | -2.1% | -1.5% | -1.8% | -1.9%

## Slide 39: Transition Phase 1

## Slide 40: Transition Phase 1
Phase 1 involves using ME for life-cycled and APB new/reconstruct projects
Normal review processes: MDOT internal, industry, EOC
Construction Field Services will be producing a detailed report on each project design: inputs used, design results, reasons for each iterative design, etc.

## Slide 41: Transition Phase 1
Phase expected to go through August
Summary report on design results to be provided to EOC
  EOC approval needed to move on to next phases

## Slide 42: Transition Phase 1
Performance Criteria | Limit | Reliability
Initial IRI (in./mile) | 67 | 95%
Terminal IRI (in./mile) | 172 | 95%
Top-Down Fatigue Cracking (ft/mile) | Not Used | Not Used
Bottom-Up Fatigue Cracking (percent) | 20 | 95%
Transverse Thermal Cracking (ft/mile) | 1000 | 95%
Total Rutting (in.) | 0.5 | 95%
Asphalt Rutting (in.) | Not Used | Not Used
HMA Design Thresholds:

## Slide 43: Transition Phase 1
Performance Criteria | Limit | Reliability
Initial IRI (in./mile) | 72 | 95%
Terminal IRI (in./mile) | 172 | 95%
Transverse Cracking (% slabs cracked) | 15 | 95%
Mean Joint Faulting (inches) | 0.125 | 95%
JPCP Design Thresholds:

## Slide 44: ME Webpage

## Slide 45: MDOT ME Webpage
Public webpage location: Link is on Construction Field Services public webpage:

## Slide 46: ME Webpage
Direct Link:
www.michigan.gov/mdot/0,4616,7-151-9623_26663_27303_27336_63969---,00.html

## Slide 47: ME Webpage

## Slide 48
Questions?
Mike Eacker
eackerm@michigan.gov
517-322-3474
Justin Schenkel
schenkelj@michigan.gov
517-636-6006